## Slide 1: Mobile EEG - Neurofeedback
18/12/2023

## Slide 2
Considerations
Top 2 (5) mobile EEG headsets
Further options
Excel table
Outline

## Slide 3: Considerations

## Slide 4
mobile system (→ wireless)
data quality
max. £ 6,000
covers motor cortex
flexibility (electrode positions)
Non-negotiables

## Slide 5
n channels
dry vs. saline vs. wet electrodes
active vs. passive electrodes
sfreq
TTL (hardware trigger - time synchronisation)
AUX (photoresistor – time sync) and bipolar channels (EMG)
battery life
Technical considerations

## Slide 6
setup time
setup difficulty (can patients do it themselves?)
comfort
cap sizes
Design considerations

## Slide 7: Top 2 mobile EEG headsets

## Slide 8: g.Nautilus + g.Sahara Hybrid
Manufacturer: g.tec medical engineering GmbH
Cost: £ 4,850 – 5,400
8 channels - active electrodes – dry or wet (!)
sfreq: 250 or 500 Hz
Layout: 74 position - extended 10/20 system
+ 86 intermediate positions

## Slide 9: OpenBCI Ultracortex Mark IV
Manufacturer: OpenBCI
Cost: £ 2,750-3,000
16 channels - dry active / wet passive electrodes
sfreq: 125 Hz (1000 Hz)
Layout: flexible but requires CAD + 3D printing

## Slide 10: Active EEG Electrode Bundle
Cost: £ 3,000
dry active electrodes
electrical shielding of cables
Biosensing R&D Bundle
Cost: £ 2,900
wet passive electrodes
no electrical shielding of cables

## Slide 11
https://conscious-labs.com/eeg-devices/6-4-channels-eeg-headphones.html
Sample EEG recording
This EEG Sample shows a comparison between wet passive gold cup electrode (blue curve, used as the reference), and ThinkPulse (red curve) at the same location on occipital O1.
Signals were also compared in spectral readings: they show similar performances. This is made possible thanks to our active electronics, which provides important noise limitation.
Low noise sensor
ThinkPulse active EEG sensor SNR has been compared with respect to a state of the art EEG wet electrode. Each data presented on the histogram (channel 1 & 2) is the result of a 4 measurements average. The “Average” tag is the result of both channel 1 & 2 averaging.
The wet electrodes considered here is a gold-plated one, used with conductive paste for application on the scalp. SNR is given as a power ratio in Alpha-Waves spectral band. It has been measured with respect to Conscious Labs ThinkPulse User Kit.
OpenBCI electrodes
ThinkPulse: active dry
Goldcup: passive wet

## Slide 12: g.Nautilus Research
Cost: £ 4,852
g.Nautilus Multi-Purpose
Cost: £ 4,943
8-4 EEG + 0-4 EMG possible
g.Nautilus Pro Flexible
Cost: £ 5,395
Medical validation
Extensibility: more/other EEG electrodes, EMG

## Slide 13: Further mobile EEG headsets

## Slide 14
Emotiv: Flex Neuroelectronics: Enobio Wearable Sensing: NeuSen W mBrainTrain: Smarting (PRO)
OpenBCI: gelfree cap Bitbrain: Versatile EEG ANT neuro: waveguard net Brain Products: actiCAP

## Slide 15
Emotiv: EPOC CGX: Quick-20r v2 Wearable Sensing: DSI-24
Bitbrain: Hero Zeto WR19 Cortex Machina: Vortex or …

## Slide 16: Thank you!